## Slide 1: T2: MODELLING AND ANALYSIS OF AD-HOC NETWORKS
Justin P. Coon
Orestis Georgiou
Carl P. Dettmann
https://goo.gl/4XwEcf
August 25th 2015
CNET-ICT-318177
Slides available at

## Slide 2: Introductions
Clemson University
University of Bristol
Research Manager at Toshiba TRL
Associate Professor
Oriel College
University of Oxford
University of Melbourne
University New South Wales
Northwestern
Copenhagen University
Rockefeller University
Professor
University of Bristol
University of Nottingham
University of Bristol
Max Planck Institute
for the Physics of Complex
Systems (MPIPKS)
Senior Researcher
Toshiba TRL - Bristol

## Slide 3: Dense Cooperative Wireless Cloud Network DIWINE - FP7 EU project 2013-2015 - €4m
Dense relay/node scenarios
Wireless Network Coding (WNC)
Distributed Synchronisation
Self-contained Wireless Cloud Network (WCN)
Source and destination are blind to the cloud network
Cloud self-organising and self-processing
“This concept facilitates energy-efficient, high-throughput and low-latency network communications performed directly at the physical layer, and is capable of operating in complicated, dense, randomly defined network topologies and domains”
Smart metering networks
Critical industrial control and monitoring applications

## Slide 4: Tutorial Outline
Introduction / Motivation - OG
  Why, when and where decentralized can be better? Example applications
Modelling Random Networks - OG
  Setup and definitions, Network observables (coverage, node degree, k-connectivity)
From Infinite to Finite Networks - CD
  Asymptotics, Boundary effects, Examples
  Complex and fractal geometries
Advanced Topics - JC
  Scaling laws, Directional antennas, Small openings
Future directions and challenges - JC

## Slide 5: Ad hoc Networks key ingredients
Decentralized (no central BS but scalable)
No pre-existing infrastructure
Self-configuring "on the fly" - anywhere, anytime
Multi-hop Routing (dynamic and adaptive)
  Table-driven (proactive) routing
  On-demand (reactive) routing
  Hybrid (both proactive and reactive) routing
  Hierarchical routing protocols (tree-based)
Mobility (MANETS & VANETS)
SmartPhone (SPANs) P2P-like, Bluetooth, WiFi-direct, LTE-direct

## Slide 6: Applications of ad-hoc networks
Standardized under: IEEE 802.15.4
  ZigBee, WirelessHART, ISA100.11a, and MiWi
Wireless sensor networks (WSN)
  Environmental, Agricultural, Industrial, Military
  Disaster relief solutions
Building automation
  Smart metering, Industrial control
Internet of Things

## Slide 7: Tutorial Outline
Introduction / Motivation
  Why, when and where decentralized can be better? Example applications
Modelling Random Networks
  Setup and definitions, Network observables (coverage, node degree, k-connectivity)
From Infinite to Finite Networks
  Asymptotics, Boundary effects, Examples
  Complex and fractal geometries
Advanced Topics
  Scaling laws, Directional antennas, Small openings
Future directions and challenges

## Slide 8: Modelling ad hoc (random) networks
A statistical framework

## Slide 9: Modelling ad hoc (random) networks
  Power control
    Cooperation - signalling overheads
  MAC protocols
    TDMA / FDMA / CDMA /SDMA ...
    ALOHA / CSMA / CD / CA (802.11)
  Number and Location of wireless devices
    Ad hoc, mobile, physical constraints and costs
  Multipath (fast fading)
  Shadowing (slow fading)
  Directional antennas
  Multiple antennas
  Transmission scheme (MRC / STBC)

## Slide 10
Random geometric network
Notes: A random geometric network consist of a collection of points which are randomly scattered over a region of space according to some probability distribution in this case uniformly.
Any two points separated by a distance less than a certain specified value are said to be connected and group together to form a cluster.

## Slide 11
Random geometric network
1. G. Gilbert, “Random plane networks,” SIAM J., vol. 9, no. 4, pp. 533–543, 1961.
4. M. Walters, “Random Geometric Graphs,” in Surveys in Combinatronics 2011 (Robin Chapman, ed.), Cambridge University Press, 2011
2. M. D. Penrose, “Random Geometric Graphs”, Oxford University Press, 2003.
3. M. Franceschetti, R. Meester, ”Random networks for communication: from statistical physics to information systems”. Vol. 24. Cambridge University Press, 2008.

## Slide 12
What is the probability of achieving a fully connected network at a given density?
Confined Random geometric networks

## Slide 13
Probability of Full connectivity
The goal is to develop a theory for that is able to provide useful analytic and physical insight which can support a variety of connectivity models, and can act as a basis for further development and analysis. To this end we will derive a general formula for which is simple, intuitive and practical.
Confined Random geometric networks

## Slide 14
  Ad hoc networks - applications and standards
  What is a random geometric network?
  Stated the problem of Full connectivity in spatially confined domains
Introduction / Motivation
A short summary:

## Slide 15: Pairwise Connection function
Complement of outage probability
Path loss attenuation function
Path loss exponent
Total Interference at j
Interference factor
M. Haenggi. Stochastic geometry for wireless networks. Cambridge University Press, 2012.
F. Baccelli, and B. Blaszczyszyn. Stochastic geometry and wireless networks: Theory. Vol. 1. Now Publishers Inc, 2009.
Channel gain

## Slide 16
Hard = Deterministic
Soft = Stochastic/Probabilistic
Rayleigh Fading
Pairwise Connection function

## Slide 17: Pairwise Connection function
Rayleigh Fading
Rician Fading
(CLT)

## Slide 18: Pairwise Connection function
Complement of outage probability
Path loss attenuation function
Path loss exponent
Channel gain

## Slide 19: Pairwise Connection function
H is the pair connection function: the probability that two nodes are directly “connected”
Deterministic
Probabilistic
Randomness (is good):
  Number and Location of wireless devices
  Multipath (fast fading)
  Directional antennas
  Multiple antennas

## Slide 20: Anisotropically radiating nodes
Patch
Dipole
Horn
Normalization:
C.A. Balanis, Advanced engineering electromagnetics. Vol. 111. John Wiley & Sons, 2012.
Antenna Tx
and Rx gains

## Slide 21: Anisotropically radiating nodes
Patch
C.A. Balanis, Advanced engineering electromagnetics. Vol. 111. John Wiley & Sons, 2012.

## Slide 22: Multiple antennas
1) Single Input Single Output (SISO)
2) Single Input Multiple Output (SIMO/MISO)
3) Multiple Input Multiple Output (MIMO-MRC) with 2 receiving and n transmitting antennas (or vice versa)
m=2, 2, 4, 4
n=2, 5, 10
η=2, 2, 6
η=2, 3, 2, 3

## Slide 23: Multiple antennas
SISO:
2) Single Input Multiple Output (SIMO/MISO)
m=2, 2, 4, 4
η=2, 3, 2, 3
χ2 distributed with 2mn dof
MIMO: (STBC)

## Slide 24
A Statistical framework
Pairwise Connection probability
  Soft vs Hard
  Rician and Rayleigh fading
  Directional antennas
  Multiple antennas
Modelling ad hoc (random) networks
A short summary:

## Slide 25
Local Network Observables
The probability of some node i connecting with some other node
The probability that node i connects with exactly k other nodes - degree distribution
Pair formation probability: The probability that two randomly selected nodes connect to form a pair
Mean degree

## Slide 26
2-node correlation function
2
3
1
Nearby nodes are less correlated for soft connectivity functions
Probability that node 1 connects with node 3, given that node 1 is connected with node 2:
Local Network Observables
η = 2, 4, 6, ∞

## Slide 27
A cluster expansion in 3 simple steps
1) Start with the probability of two nodes being connected (or not)
2) Multiply over the complete graph to get the probability of all possible combinations giving 2N(N-1)/2 terms
3) Group into collections of terms determined by their largest cluster
4) At high densities full connectivity is simply the complement of the probability of an isolated node.
Full Connectivity: Corners, edges and faces, Journal of Statistical Physics, 147 (4), 758-778, (2012)
Global observables:
Given a graph, what is the probability of achieving full connectivity?
A graph is fully connected if there exists at least one multi-hop path connecting every two nodes.
(Erdӧs 1959)

## Slide 28
Step 1
Start with the probability of two
nodes being connected (or not):
i
j
Step 2
Multiply over the complete graph to get
the probability of all possible combinations:
Step 3
G3, 1
G3, 2
G3, 3
3. Group into collections of terms determined by their largest cluster:
At high densities, full connectivity is the complement of an isolated node:

## Slide 29
Define an average over all possible configurations
1) Node N is not connected to any of the other N-1 nodes
2) Multiply by N since all nodes are identical
3) Since we are comparing pairs of nodes, N-2 integrals can be decoupled through a change of variables:
A cluster expansion in 3 simple steps

## Slide 30
The Homogeneous case
Assuming that the network is homogeneous, implies that there are no boundaries and therefore the system is symmetric under translational transformations. This allows for a final change of variables and we are left with a single integral:
Example of a homogeneous network space: Surface of a Sphere

## Slide 31
k-connectivity: network remains fully connected if any k-1 nodes are randomly removed
K-connectivity - Reliability
1-connected
2-connected
3-connected

## Slide 32
The probability of network having minimum degree k
k-connectivity for confined random networks, Europhysics Letters, 103, 28006, (2013)
K-connectivity - Reliability
(1 - probability node has degree at most k-1)^N

## Slide 33
Q. What about ?
X(1) = probability of obtaining a fully connected network which is not 2-connected.
At high densities, a fully connected network which is not 2-connected will typically contain a single node which is of degree 1.
Repeating this argument k times:
Since 2-connectivity implies 1-connectivity
A. and have the same asymptotic distribution.
K-connectivity - Reliability

## Slide 34
The probability of network having minimum degree k
K-connectivity - Reliability

## Slide 35
A cluster expansion in 3 simple steps
Full connectivity (homogeneous case)
Local Network Observables
  Pair formation
  Mean degree
  2-node correlation function
k-connectivity
Modelling ad hoc (random) networks
A short summary:
1-connected
2-connected
3-connected

## Slide 36: Tutorial Outline
Introduction / Motivation
  Why, when and where decentralized can be better? Example applications
Modelling Random Networks
  Setup and definitions, Network observables (coverage, node degree, k-connectivity)
From Infinite to Finite Networks
  Asymptotics, Boundary effects, Examples
  Complex and fractal geometries
Advanced Topics
  Scaling laws, Directional antennas, Small openings
Future directions and challenges